## Slide 1
Alexander Kiselev
EIC R&D Tracking Meeting
Oct,26 2015
Towards “optimal”
GEM zigzag
readout plane layout
part#2

## Slide 2: Contents of these presentations
part#1: motivation; ideas; goals; linear strip case (ideal model)
part#2: RICH GEM readout plane layout optimization
part#3: linear strip case (ANSYS modeling)
-> this talk!

## Slide 3: Motivation
Spatial resolution of the present GEM pad layout noticeably affects Cerenkov ring radius resolution:
Too small electron cloud size
Too big pads
-> basically no charge sharing (so effectively single pad - “digital” - mode)
-> the intention is to arrange charge sharing between neighboring pads, perhaps in a way similar to the straight strip case (see talk#1)

## Slide 4: Simulation environment
Custom ROOT script, mostly unified with the straight strip case
Same as in talk#1: assume 100% of readout plane covered by pads -> so cloud electron originated at the point (x,y) below the bottom GEM foil will be registered by the pad which geometrically contains point (x,y) in the readout plane; in other words: no electric field distortions need to be accounted
Same as in talk#1: use gaussian distributions; ignore GEM foil holes; no cross-talk effects accounted (to this moment)
-> this is no way a complete simulation, but rather a tool to indicate possible way(s) of readout pad geometry optimization

## Slide 5: Simulation & analysis configuration
Default (basic) parameters:
Fixed ring radius of 33 mm; ring centers uniformly spread over a single pad area
10 photons per ring (Poisson distribution)
Gain ~103 (CPU-driven, sufficient to avoid low statistics bias; all charge cloud electrons simulated individually: 2D gaussian distribution)
Charge cloud footprint size: 130 microns
Hexagon-like pads with 5mm diagonal
Noise level of ~6% to the signal amplitude
All p.e. handled separately (good enough for this simple study?)
Assume ring center location is known
Typically work with 1x noise level threshold

## Slide 6: Validation plots (“hexagon” mode)
10 p.e. per ring
Ring radius 33 mm
Resolution ~400 mm
-> will take ring radius resolution estimate of ~400 microns as a reference value (baseline) in the following modeling
NB: there are several other effects which influence Cerenkov angle reconstruction
Readout pad spatial resolution is only one of them; if it can be improved by a factor of ~2 or so without much of a complication, it must be already good enough (see fig15 in arXiv:1501.03530v2)

## Slide 7: “Precision snowflake” readout pad
The first idea is ~trivial: replace straight borders between neighboring hexagons by “diamond bands” with linear weighting scheme (see talk#1):
(Almost) always have sufficient charge sharing (so a cluster of 2 neighboring pads)
If only a single pad is above threshold, p.e. must have hit this pad “center” -> fine
3-pad clusters can only improve resolution further (not considered in this study)
Therefore can typically identify a rhombus (defined by two cluster pads), which immediately decreases p.e. impact hit area by a factor of 3 compared to a hexagon
If linear weighting scheme can be implemented properly, 1D coordinate along the line connecting two cluster pad centers can be determined with a reasonably high precision, which in theory should further improve ring radius resolution

## Slide 8: Weighted mean centroid for this pattern
-> ~300 mm resolution is poor, yet better than ~1mm in case of no charge sharing!
NB: residual plot range is 4mm here!
NB: X-range is 1 strip wide here!
X-pitch is just the hexagon pad-to-pad distance, so ~4.33mm
Y-period: ideally at most 2x130 mm (see talk#1, p.31; consider geometric scaling); this is hardly feasible -> so take 400 mm (which is yet a bit too optimistic); NB: actually the intrinsic spatial resolution is so bad, that this expansion has only a minor effect
2-pad clusters (would see ~400 mm if used 3-pad ones, see talk #1, pp.30&31)
Noise level of 6%; it is very high (bad for the spatial resolution, but turns out not to be the dominant factor for ring radius measurement anyway)
NB: “tails” in the 2D plot around “strip center” locations (effect of 2-pad selection) are irrelevant, since these spots will be occupied by solid pad centers anyway

## Slide 9: “Precision snowflake” readout matrix
-> NB: tree “trunks” are not implemented and small spots in the middle of each pad are not shown here
The more “fine” the structure can be manufactured the better, but this one is perhaps already at the edge (Y-pitch-equivalent parameter is 2.5mm/6 ~ 417mm here)
NB: see talk#1, p.47 for the suggested manufacturing limits

## Slide 10: Pattern builder
-> trivial, robust and versatile: works pretty much the same way for pads with linear and azimuthal cloning algorithms; drawing functionality is as close to “pad->IsInside(TVector2 &point)” calls in the code as possible (so that what one sees in the pictures are hopefully exactly the patterns which govern distribution of cloud electrons over readout pads in the simulation)
polygon
pattern
pad
matrix
In case you were wondering: no, it is not a CorelDraw output ; basically a collection of simple custom C classes in ROOT

## Slide 11: Event simulation sequence
Uniformly simulate ring center XY-coordinates inside a hexagon area located at (0,0)
Simulate photon count (according to Poisson distribution)
For each photon separately:
Simulate asimuthal angle
Simulate N electrons according to the pre-defined gain (sample 2D gaussian distribution with given fixed sigma around photon location -> obtain XY-coordinates -> allocate each electron to the pad which contains these (x,y) -> so accumulate expected charge per pad)
Simulate noise (sample gaussian with 0 mean and given sigma) for each pad separately and add to the accumulated charge
Estimate ring-center-to-photon distance and respective 2D covariance matrix (see next slide)
Estimate ring radius as a weighted mean over all photons (where covariance matrices are projected onto the respective ring-center-to-photon direction)
-> these two pages are for the sake of completeness only …

## Slide 12: Single photon reconstruction sequence
Select pad with the highest accumulated charge
If there are no neighboring pads with charge above given threshold, consider a single pad cluster: take photon coordinates as the center of this pad
If there is (are) neighbor pad(s) above threshold, take only the one with the highest charge and consider a two-pad cluster with the “main” pad
If in “rhombus reconstruction mode”, take photon coordinates right in between of the two cluster pads; in “zigzag reconstruction mode” calculate coordinate along pad-to-pad direction according to the linear weighting scheme using accumulated charges as weights
Covariance matrices:
in “rhombus” mode all weights are taken to be 1.0 (no tricks)
in “zigzag mode” single-hit clusters will be assigned a symmetric covariance matrix roughly matching pad central spot size; two-pad clusters will be given properly oriented diagonal 2D matrices with roughly “diamond band”-equivalent resolution in one direction and rhombus-width-matching resolution in the other one

## Slide 13: “Snowflake”: ring radius resolution
rhombus mode: ~250 um
Make estimates for this “ideal” pattern first
-> so indeed it works: compare to ~400 mm in hexagon (binary) mode
zigzag mode: ~170 um

## Slide 14: A more realistic “precision snowflake”
Narrow spikes are “no go” for the manufacturing; also a solid spot is needed at the center of each pad anyway; so allocate a hexagonal area with a side 2.5/2 = 1.25mm there
There are no essential “features” <100 mm in this design; so it is “almost doable” except for the fact one needs to find space for the strip-to-strip gaps 
-> surprisingly enough, this modification does not really make the ring radius resolution of ~170 mm in the “zigzag” mode worse, so use this pattern for the next 2 slides

## Slide 15: Realistic “snowflake”: spatial resolutions
Resolution of the 1D distance in pad-center-to-pad-center direction is ~300 mm, as expected (see slide #8)
By fine tuning ring radius resolution can in fact be improved a bit towards ~160 mm or slightly better; here this is just an effect of a higher threshold
-> NB: this higher threshold is applied (2x noise level) in order to clean up the 1D distance plot

## Slide 16: “Snowflake”: ring radius resolution
… as a function of e- cloud width
… as a function of pedestal noise
-> default configuration
Clearly this configuration is at the edge of performance in terms of cloud-sigma-to-Y-period ratio
Contrary to the similar plot in talk#1: pretty low sensitivity to noise level (see explanation on p.24)

## Slide 17: “Snowflake”: ring radius resolution
… as a function of Y-period
… as a function of threshold
-> charge spread becomes insufficient to wash out periodic structure effects in the Y-direction
Almost no sensitivity to the threshold setting in the reconstruction
Another view on the effect of the cloud-sigma-to-Y-period ratio: due to the small electron cloud footprint size can not go to the technologically more comfortable “diamond band” pattern with bigger Y-period

## Slide 18: Another option: a “robust snowflake”
Forget about “precise” 1D coordinate measurement and focus on reliably getting ~50:50 charge sharing in “zebra” overlap regions
Use snowflakes with straight spikes, and possibly push the structure period further down (2.5mm/8 ~ 312 mm here, yet certainly doable) …
-> does not require (almost) any further thinking and may pretty much be the best choice 

## Slide 19: Another option: a “robust snowflake”
… thus always restrict photon hit area by a small hexagon with 1.25mm long side
Yes, this option gives ~200 mm ring radius resolution, a plain factor of two compared to the “big hexagon” mode
NB: will either have to raise threshold in the reconstruction sequence (here x2 in noise units) or use the strong amplitude correlation in two pads composing the cluster if “zebra” area is hit

## Slide 20: Shopping list: baseline
Present design (~400 mm)
Advantage: robust (“digital” mode), no need to change anything 
Drawback: poor spatial resolution
-> listed here only to determine relative resolution scale for comparison with the other options in the considered simulation environment

## Slide 21: Shopping list: option #1
“Rhombus mode” (~250 mm)
-> as simple and appealing as it is, not the optimal solution
Advantages: robust (“digital mode” once overlapping pads are identified); immediate areal resolution improvement by a factor of ~3 (which naturally translates into respective improvement in 1D ring radius resolution)
Drawbacks: per design serves only as a fallback solution for the snowflake model with linear charge sharing; “optimal” implementation is not feasible (too narrow spikes); and if one goes for more robust straight strips (no longitudinal 1D coordinate measurement), option #3 is better

## Slide 22: Shopping list: option #2
“Precision snowflake” (~170 mm)
Advantages: highest ring radius resolution out of the configurations considered so far; if can be implemented properly in hardware, achievable resolution level is not much sensitive to the noise level and threshold setting
Drawbacks: given small charge cloud footprint and technological limits, implementing either “ideal” linear charge sharing model or some other one which would work well requires careful electrostatic modeling; may be more sensitive to field distortions due to the GEM foil holes, to overlapping photon signals and other subtle effects; improvement in 1D spatial resolution does not immediately translate into the ring radius resolution increase (see respective comment on the “2D charge sharing” slide as well);
-> would become much more attractive if electron cloud was ~200 mm

## Slide 23: Shopping list: option #3
“Robust snowflake” (~200 mm)
Advantages: robust (sort of “digital” mode); clearly can be implemented in hardware (as long as increased capacitive coupling does not cause some performance degradation); does not require electrostatic modeling; a factor of x2 spatial resolution improvement “now” & “almost for free”
Drawbacks: limits possible resolution improvement to the design factor of x2 (so if that is not enough, one has to decrease pad-to-pad distance); does not benefit from either reduced pedestal noise or electron cloud size increase should they become possible
-> if a factor of x2 is enough, the best choice?

## Slide 24: 2D charge sharing?
Consider to arrange coarse 2D coordinate measurement: in every inter-pad triangle (see the drawing) place 3 long variable width “polyline” strips “growing” from their respective pad centers
So pretend to typically have 3-pad clusters with an option of relatively low resolution 2D coordinate measurement using non-linear charge sharing model
This would allow to overcome the obvious problem of 1D coordinate measurement with “precision snowflakes”: no matter how good 1D resolution is, if respective rhombus is oriented at an angle to photon-to-ring-center direction, radius resolution is dominated by finite (and large!) rhombus width
-> this is doable; but 1) requires much more thinking & modeling, 2) poses technological challenges like usage of 50-75 mm feature and gap sizes; however potentially this layout can give best results, if resolution really needs to be pushed to its limits

## Slide 25: Option #2 + 2D charge sharing
Just to mention: one can perhaps arrange somewhat smaller 3-pad-overlap triangles shown on the previous page in order to effectively cut away rhombus edges along the short diagonal in the “precision snowflake” design for the cases when photon hits “zebra” pad overlap area
This would probably allow to partly overcome the problem of 1D coordinate measurement in “precision snowflake” model explained earlier and go below 150 mm ring radius resolution in this simulation environment

## Slide 26: Outlook
Effects of increased strip-to-strip capacitance need to be estimated
Cross-talk model should better be implemented in the code
Gaps are necessary between strips (and feasibility of linear charge sharing model is questionable); if “precision snowflake” model is of interest, the answer will become more clear once straight strip case is elaborated in more detail
Non-gaussian cloud shapes should be checked (effect of GEM holes, etc), although the impact (in particular for 50:50 charge sharing configuration with straight strips) must be small